## Slide 1: Module-6
Drilling

## Slide 2: Module Objectives
1. Describe the operation of a drill press.
2. Identify the drill press parts.
3. Identify the parts of a twist drill.
4. Determine the drill size by measurements or direct reading.
5. Identify the drill and work holding devices.
6. Describe and follow the procedure when performing the drilling operation.
7. Explain and apply the safety rules that should be followed before and during the drilling operation

## Slide 3: Introduction
Drilling is used to create round holes

## Slide 4: The Main Parts of The Floor Drill Press
The floor (pedestal) drill
press is a drill press
which sits on the floor.
It is used to drill
small to medium sized holes
and other light drilling operations
Feed Handle
Motor
Head
ON/OFF switch
Chuck
Table
Base
Column
Table Handle

## Slide 5: Twist Drills
The most common tool used in a drill press to cut a hole is the twist drill
The twist drill is a rotary cutting tool that is made of a piece of round steel stock. The cutting edges down near the point of the drill cut away materials the drill is moved into contact with the work piece.
The main parts of the twist drill are listed below and are.
1. Shank
2. Body
3. Point
4. Web
5. Tang

## Slide 6: Types of Drill shanks
Drills are classified according to the shape of the shank into two main types:
i)Straight (Parallel) shank drill
ii)Morse taper shank drill

## Slide 7: Straight (Parallel) shank drill
Straight shank or parallel shank drill is
shown in Fig.
Most of small drills up to 13 mm in
diameter have straight shanks.

## Slide 8: Morse taper shank drill
Morse taper shank drill is shown in Fig.
Tapered drills are supplied in
diameters ranging from 3 mm to 100
mm diameter.
Most drills that are
larger than 13 mm are tapered.

## Slide 9: Determining The Drill Size
Most drills have the diameter size stamped on the shank.
However, generally, the micrometers and drill gauges are used to determine and
check the drill diameters.
Fig 6.5. shows a drill gauge that is used to
determine the drill bit size.

## Slide 10: Drill-Holding Devices
The holding device is used to hold
the drill during the drilling operation.
There are two main methods to hold
the drill.
Chucks
Tapered spindles

## Slide 11: 1. Chucks
The chuck is an adjustable moving
jaw mechanism mainly used for
drills with straight shanks. The
chuck and chuck key are shown in

## Slide 12: 2. Tapered spindles
A tapered opening is used
for drills with taper shanks.
The drill is locked in the spindle with
friction and is removed from the
spindle by using a drift as shown .

## Slide 13: Work-Holding Devices
Work-holding devices are used to hold the work piece during the drilling operation.
The work holding devices are:
1. Vises
2. T-bolts and Clamps

## Slide 14: 1. Vises
Vises are widely used to hold the
work piece during the drilling process. The vise must be bolted to the drill table to ensure a safe and proper practice as shown.

## Slide 15: 2. T-bolts and Clamps
The T-bolts and clamps are used to hold a round work piece onto the drill press table as shown.

## Slide 16: Cutting Speed and Different Materials
Cutting speed is the speed at the outside edge of the tool as it is cutting the work piece.
Cutting speeds depend on the type of material being cut and the type of cutting tool being used.
. The harder the work material, the slower the cutting speed. The softer the work material, the faster the cutting speed.

## Slide 17: Drilling Procedures
I.Before drilling (while the machine is powered off)
1. Wear the safety gear
2. Use measuring tools and layout tools to locate the centers of the holes
to be drilled.
3. Use a center punch to make an indentation (marking) at the centers of
the holes locations.
4. Determine the drill size to be used.
5. Place the drill in the chuck or drilling machine spindle.
6. Tighten the chuck with a chuck key, or turn the shank until the tang
fits in the slot.
7. If a chuck is used, remove the chuck key as shown in Fig. 6.12.
8. Adjust the table to the desired height by using the table handle.
9. Turn the feed handle to lower the drill. Ensure that the drill can be
lowered enough to drill the hole as shown in Fig. 6.13.
10. Use the work-holding devise to secure the material to be drilled.
11. Set the drilling machine to the correct speed.
12. Turn the feed handle to align the first center punch mark under the
drill.

## Slide 19: During drilling (while the machine is turned on)
1. Turn the feed handle to lower the drill to the material.
2. Apply light pressure to the feed handle to start drilling the hole. Be
careful that too much pressure could break small drills.
3. Withdraw the drill and turn the drilling machine off.
4. Remove the work piece from the table.
5. Remove the drill, store the drill in its proper place and clean the drilling
machine table using a brush.

## Slide 20: Drilling Safety
1. Know the position of the emergency stop.
2. Wear all the safety gear required for the job.
3. Make sure the chuck key is removed.
4. Tighten the clamps, vise and table locks.
5. Do not wear loose clothing (wear overall).
6. Do not hold the work in your hand (use a clamp).